## Slide 1
Σ
SIGMA
Segmentation & Image Guided Medical Annotation
View and segment DICOM and NIfTI volumes in your browser — no desktop install required.
How-To Guide

## Slide 2
What is ΣIGMA?
A browser-native ITK-SNAP alternative for researchers and radiologists
Viewer
• Axial, Coronal, Sagittal + Oblique
• Synchronized crosshairs
• Single-panel zoom mode
• Window / Level presets
Editor
• Paint & erase segmentation masks
• Region grow (Grow2D)
• Fill holes, clear slice
• Undo (3 levels)
Workflow
• Folder-based volume catalog
• DICOM & NIfTI support
• Save masks as NIfTI
• AI segmentation integration

## Slide 3
Getting Started
Install once, then just run start.sh
1
Clone the repo
git clone https://github.com/slowvak/SIGMA.git
2
Set up the Python environment
cd server && uv sync
3
Install frontend dependencies
cd client && npm install
4
Launch both servers
./start.sh → open the URL shown in the terminal
Prerequisites: uv (Python package manager) and Node.js + npm

## Slide 4
Opening a Volume
Click Open Folder
Select any directory on your filesystem — ΣIGMA scans it automatically for DICOM series and NIfTI files.
Pick a volume from the list
The left panel shows every discovered series. Click one to load it into the viewer.
Wait for the progress bar
Volume data streams from the local server into browser memory. Large CTs take a few seconds.
Use Back to Volumes to return
Switch volumes at any time without restarting the server.

## Slide 5
The 4-Panel Viewer
Axial · Coronal · Sagittal · Oblique — all synchronized
Axial
Coronal
Sagittal
Oblique
Scroll slices
Mouse wheel or click-drag up/down on any panel
Crosshair sync
All panels update instantly when you click with the crosshair tool
Single-panel mode
Click the panel's name label (A / C / S) to expand it full-screen; press 4 to restore
Slice slider
The bar below each panel lets you jump to any slice position
Oblique panel
Always shows the plane defined by the current crosshair intersection

## Slide 6
Window / Level
Adjust image contrast and brightness for your tissue of interest
Right-click drag on any viewer panel:
← → (left / right)
Changes Window width (contrast)
↑ ↓ (up / down)
Changes Level / centre point (brightness)
Quick Presets
Brain
W 80 L 40
Bone
W 2000 L 400
Lung
W 1500 L -600
Abdomen
W 350 L 40
Current W/L values are shown in the tool panel at all times.

## Slide 7
Segmentation Tools
✛ Crosshair
• Navigate across all panels simultaneously
• Click to set crosshair; all views re-centre
✏ Paint
• Left-click drag to paint the active label
• Brush Radius slider controls size
• Brush Depth paints through N adjacent slices
• Intensity Limits restrict painting by HU range
⊕ Grow2D
• Click a seed voxel on the current slice
• Expands to connected voxels within Min–Max intensity
• Range auto-sets to mean±stdev of 5×5 patch around seed
• Adjust with the dual slider or type values directly
⊘ Erase
• Select Erase mode in the label panel
• Brush removes voxels of any label

## Slide 8
Actions
Operations in the toolbar that modify the segmentation
Undo (Ctrl+Z)
Reverts the last paint, grow, refine, propagate, or fill operation. Supports up to 3 levels of undo.
Refine
Snaps the active label boundary to image edges on the current axial slice using Sobel gradient detection.
Propagate
Copies the label from the adjacent slice and refines it — use this to step through a stack slice by slice.
Fill Holes
Fills enclosed background regions within each connected component of the active label on the current slice.
Clear Slice
Removes all voxels of the active label on the current slice only. Useful for restarting a single slice.
Filter
Smooths raw image intensities. Choose 2D/3D, Mean/Median/Sigma (Gaussian), kernel size 3/5/7, Slice or Volume.
Save As…
Writes the current segmentation back to the server as a NIfTI (.nii.gz) mask file.

## Slide 9
Managing Labels
The label panel lives on the right side of the toolbar
Single-click a label
Makes it the active label for painting, erasing, and all segmentation operations.
Double-click a label
Opens the label editor — rename the label, change its colour, or delete it.
Eye icon
Toggle the visibility of a label in the overlay without changing which label is active.
Colour swatch
Quick-click to change a label's display colour directly from the list.
+ button
Add a new label. Prompts for a name and auto-assigns the next available colour.
Label Overlay Opacity
Slider (0–100%) controls how opaque the segmentation colour overlay appears over the image.

## Slide 10
AI Integration
Accelerate segmentation with automated models
Click the 🤖 AI button in the toolbar to open the model picker.
TotalSegmentator
Downloads the current volume as a NIfTI file and opens totalsegmentator.com for full-body auto-segmentation. The result can be imported back as a label file.
Server-Side Models
Custom models defined in models/ai-models.json appear in the picker automatically. Any model that accepts a NIfTI volume and returns a mask can be wired in.

## Slide 11
Keyboard Shortcuts
?
Open the in-app help panel
Ctrl + Z
Undo last segmentation edit (up to 3 levels)
Escape
Close any open modal dialog
4
Return to 4-panel view from single-panel mode
A / C / S
Click the panel label to expand Axial / Coronal / Sagittal to full screen
Mouse Wheel
Scroll through slices on the focused panel
Right-click drag
Adjust Window (left/right) and Level (up/down)

## Slide 12
Typical Segmentation Workflow
1
Open Folder
Point ΣIGMA at the directory containing your DICOMs or NIfTIs
2
Select Volume
Click the series in the left panel to load it
3
Set Window / Level
Use a preset (Brain / Bone / Lung / Abd) or right-click drag to tune contrast
4
Create / select label
Click + to add a label, or single-click an existing one to activate it
5
Paint seed
Use Paint or Grow2D to lay down your initial segmentation on a representative slice
6
Propagate
Press Propagate to copy-and-refine the label to adjacent slices, stepping through the stack
7
Clean up
Use Fill Holes, Clear Slice, or manual painting to fix any errors
8
Save
Click Save As… to write the mask back to disk as a NIfTI file

## Slide 13
Tips & Tricks
Use Intensity Limits while painting
Restrict the brush to a HU range so you only paint the tissue you intend — prevents spill-over into adjacent structures.
Grow2D + Propagate combo
Grow2D a seed on the clearest slice, then Propagate through the rest of the stack for fast, consistent labelling.
Brush Depth for thick structures
Set Brush Depth > 1 to paint through multiple slices at once — great for large uniform regions.
Adjust opacity while reviewing
Lower the Label Overlay Opacity to see the underlying image anatomy while checking your mask boundaries.
Double-click to rename
Double-click any label in the panel to rename it, change colour, or delete — keep labels descriptive from the start.
Filter before growing
Apply a 2D Gaussian (Sigma) filter to noisy slices before using Grow2D — the smoother intensity surface yields cleaner region boundaries.